## Slide 1: Back-Projection on GPU: Improving the Performance
Wenlay “Esther” Wei
Advisor: Jeff Fessler
Mentor: Yong Long
April 29, 2010

## Slide 2: Overview
CPU vs. GPU
Original CUDA Program
Strategy 1: Parallelization Along Z-Axis
Strategy 2: Projection View Data in Shared Memory
Strategy 3: Reconstructing Each Voxel in Parallel
Strategy 4: Shared Memory Integration Between Two Kernels
Strategies Not Used
Conclusion

## Slide 3: CPUs vs. GPUs
CPUs are optimized for sequential performance
  Sophisticated control logic
  Large cache memory
GPUs are optimized for parallel performance
  Large number of execution threads
  Minimal control logic required
Most applications use both GPU and CPU
  CUDA

## Slide 4: Original CUDA Program
Back-projection of FDK cone-beam image reconstruction algorithm on GPU
One kernel of nx-by-ny
Each thread reconstructs one “bar” of voxels with the same (x,y) coordinates
The kernel is executed for each projection view
  Back-projection result is added onto the image
2.2x speed-up for 128x124x120-voxel
image
My goal is to accelerate this algorithm
Notes: Because voxels with the same (x,y) coordinates share a lot of same computations such as s-indices on detector

## Slide 5: Strategy 1: Parallelization Along Z-Axis
Eliminates sequential components
Avoids repeating the computations
  Additional kernel is needed
  Parameters that shared between two kernels are stored in global memory

## Slide 6: Strategy 1 Analysis
2.5x speed-up for 128x124x120-voxel image
Global memory accesses prevents an even greater speed-up

## Slide 7: Strategy 2: Projection View Data in Shared Memory
Modified version of previous strategy
Threads that share the same projection view data are grouped in the same block
Every thread is responsible for copying a portion of data to shared memory
Each thread must copy four pixels from the global memory otherwise the results would be approximate

## Slide 8: Strategy 3: Reconstructing Each Voxel in Parallel
Global memory loads and stores are costly operations
  Necessary for Strategy 1 to pass parameters between kernels
Trade global memory accesses with the repeated instructions
Perform reconstruction on
each voxel in parallel

## Slide 9: Strategy 3: Analysis
Does compensate for the processing time of repeated computation
Does not improve the performance overall
  2.5x speed-up for 128x124x120-voxel image

## Slide 10: Strategy 4: Shared Memory Integration Between Two Kernels
Modify Strategy 1 to reduce the time spent on global memory accesses
Threads sharing the same parameters from kernel 1 reside in the same block in kernel 2
Only the first thread has to load the data from global memory into shared memory
Synchronize threads within a block after memory load

## Slide 11: Strategy 4 Analysis
7x speed-up for 128x124x120-voxel image
8.5x speed-up for 256x248x240-voxel image

## Slide 12: Strategies Not Used #1
Resolving Thread Divergence
  Single-instruction, multiple thread (SIMT) style
    32-thread warps
    Diverging threads within a warp will execute each set of instructions in a sequential manner
  Thought thread divergence would be a problem and was seeking solutions
  Occupied less than 1% of GPU processing
  One of the reasons could be that most of the threads follow the same path when branching

## Slide 13: Strategies Not Used #2
Constant Memory
  Read-only memory, readable from all threads in a grid
  Faster access than global memory
  Considered copying all the projection view data into constant memory
  There are only 64 kilobytes of constant memory in the GeForce GTX 260 GPU
    A 128x128 projection view uses that much memory

## Slide 14: Conclusion
Must eliminate as many sequential processes as possible
Must avoid repeating multiple computations
Must keep number of global memory accesses should to the minimum necessary
  One of the solutions is to use shared memory
  Strategize the usage of shared memory in order to actually improve the performance
Must consider if the strategy would work on the specific example we are working on
  Gather information on the performance

## Slide 15: References
Kirk, David, and Wen-mei Hwu. Programming Massively Parallel Processors: a Hands-on Approach. Burlington, MA: Morgan Kaufmann, 2010. Print.
Fessler, J. "Analytical Tomographic Image Reconstruction Methods." Print.
Special thanks to Professor Fessler, Yong Long and Matt Lauer

## Slide 16: Thank You For Listening
Does anyone have questions?